## Slide 1
Household Level DT
A Building-Level Digital Twin for Sustainable Living
From an IFC model to an interactive, geolocated, energy-aware web twin
Twinlink.eu · 3DxVERSE D7.2 — Interoperable Digital Twin Testbed · University of Twente / ITC · Aadorp, NL
Notes: Bram House digital twin built within 3DxVERSE WP7. Presenter: Joan.

## Slide 2
CONTEXT 02
Bram House · Building-Level Digital Twin
Why this twin exists
The 3DxVERSE testbed
Deliverable D7.2 calls for an interoperable digital twin testbed. Bram House is the building-level node of the Aadorp–Almelo Local Digital Twin.
One real household
A real family home in Aadorp (Overijssel) with a full BIM model, a year of smart-meter data, solar panels, a battery and an EV — an ideal sustainable-living pilot.
Evidence, not control
The twin supports exploration and stakeholder dialogue about energy and indoor climate — it visualises evidence rather than automating the home.
1
household, fully modelled
21
rooms extracted from the IFC
366
days of real meter data

## Slide 3
DATA 03
Bram House · Building-Level Digital Twin
What the twin is built from
Every layer traces back to a real source — nothing is hand-drawn
BIM model
Revit 2023 → IFC 2x3
474 MB, full interior with furniture
21 IfcSpaces with names & numbers
Energy meters
5 CSV exports, 15-min interval
~35,000 rows each, Jun 2025 – Jun 2026
power · solar export · battery · gas · water
Dutch open geodata
PDOK aerial photo (~8 cm)
3D BAG buildings (LoD 2.2)
BAG parcel & Cesium World Terrain
Reference drawings
DXF/DWG floor plans (Level 0)
used to verify room geometry
in QGIS during export QA

## Slide 4
LOCATION 04
Bram House · Building-Level Digital Twin
Putting the house on the map
The IFC already knew where it stood — the twin just had to listen
1
Read IfcSite
The IFC's IfcSite entity stores WGS84 coordinates in degrees-minutes-seconds: 52°22′48.9″ N, 6°37′37.2″ E.
2
Verify against BAG
The national building register (pand 0141100000019888, Kerkweg 18, Aadorp) centres ~11 m away — the offset is the Revit project base point, exactly as expected.
3
Anchor everything
One shared anchor (52.380257 N, 6.626997 E) places the 3D Tiles shell, all room polygons, appliances and camera views. Heading, height and x/y offsets stay configurable.
THE ANCHOR
52.380257° N
6.626997° E
Kerkweg 18, Aadorp · Overijssel
WGS84 (EPSG:4326)
local metres → degrees:
lat ÷ 111 320 · lon ÷ 111 320·cos(φ)

## Slide 5
PIPELINE 05
Bram House · Building-Level Digital Twin
From heavy BIM to lightweight web
Three parallel tracks feed one browser application
A — GEOMETRY SHELL
IFC (474 MB)
→
Cesium ion tiler
→
OGC 3D Tiles
Streamed level-of-detail model — the browser never loads raw IFC.
B — ROOM DATA SPINE
IfcSpaces (first 53 KB!)
→
IfcOpenShell + Shapely
→
GeoJSON (21 rooms)
Footprints, floors, heights & GUIDs. All 21 rooms sat in the first 53 KB of a 474 MB file — sliced & parsed in seconds.
C — ENERGY & IAQ DATA
Meter CSVs / sensor mocks
→
Parsing & daily deltas
→
Dashboards & overlays
Cumulative meters handled as last-minus-first; strictly separated from geometry, joined by room_id.
Architecture rule: static spatial geometry never mixes with dynamic data — sensors and meters join later via room_id.

## Slide 6
SOFTWARE 06
Bram House · Building-Level Digital Twin
The application under the hood
A deliberately simple stack — no backend required for the MVP
viewer/
Cesium scene, basemaps, terrain, IFC shell, section-cut clipping, x-ray
interaction/
room navigator & state, fly/walk/patrol cameras, appliances, IAQ modes
panels/
app shell & branding, dashboard, energy charts, gamification HUD
simulation/
Time Machine replay, what-if energy scenarios
data/
energy CSV service (cumulative-meter math), sensor readings service
Vite + vanilla ES modules · CesiumJS (CDN) · Chart.js · no framework
~5,700
lines of JavaScript
30
ES modules in 5 layers
0
servers needed to run it

## Slide 7
SCENE 07
Bram House · Building-Level Digital Twin
A real place, not a floating model
The house sits in its actual street, light and terrain
IFC shell as 3D Tiles
Full-detail interior streamed from Cesium ion; manually anchored because the ion tiler ignores IFC2x3 georeferencing.
Dutch context
PDOK ~8 cm aerial photo under the house; 3D BAG neighbour buildings clipped to a 600 m box around Aadorp; the house's own BAG block filtered out by pand-ID.
Sun & shadows
Real solar position from date + time sliders — shows how light hits the PV roof in June vs December.
Section cuts
Horizontal clipping planes isolate one storey — the dollhouse view used by every room visit.

## Slide 8
ROOMS 08
Bram House · Building-Level Digital Twin
Exploring the house room by room
The IFC is what you see — GeoJSON is an invisible data spine
Building explorer
Left panel lists all 21 spaces with live IAQ chips; search, floors, appliances tab.
Fly inside
Selecting a room cuts the building open at that storey and flies to an eye-level interior view with an adaptive field of view per room size.
Walk & patrol
Press F for first-person walking (arrow keys, height control, room-entry toasts); Patrol runs a 40-second agent-style scan of a room.
IFC-first rule
Room polygons stay invisible but clickable — geometry duplicates were removed after they poked through the sloped roof.
Woonkamer · Keuken · Eetkamer · Kantoor · Tuinkamer · Bijkeuken · Wasruimte · Hal · WC ×2 · Kast — and 10 more upstairs

## Slide 9
ENERGY 09
Bram House · Building-Level Digital Twin
A year of real energy, made visible
June 2025 – June 2026 · computed from cumulative meter readings (last − first)
Chart: 
| Electricity bought (kWh) | Electricity sold (kWh) | Gas used (m³ ×10)
kWh / m³ over the year | 14094 | 5720 | 6971
Gas shown ×10 for scale (real value 697 m³)
41%
of demand offset by exporting solar surplus
4 tabs
overview · electricity · solar & battery · gas & water
15 min
meter resolution, aggregated to daily & monthly

## Slide 10
LIVING DATA 10
Bram House · Building-Level Digital Twin
Indoor air quality & appliances
Room-level and device-level views, ready for real sensors
Indoor air quality (simulated)
Per-room temperature, humidity and CO₂ with good / watch / ventilate status
CO₂ heat-map painted on room footprints
Air-patrol tour visits rooms with elevated CO₂
Future: live feed via OGC SensorThings API, joined on room_id
Appliance monitoring (mock)
10 devices placed in their real rooms — fridge, hob, washer, boiler, EV charger…
Click a marker → camera flies to it, room cut open, meter panel opens
Per-type daily profiles: EV charges at night, dishwasher at 21:00
Each panel names its appliance id — one function swap connects a smart plug

## Slide 11
ENGAGEMENT 11
Bram House · Building-Level Digital Twin
A household manager, not a CAD viewer
Gamified layers turn meter data into a story
Time Machine
Scrub or replay the whole year: rooms glow with each day's gas heating, green on solar-surplus days, chimney smoke on heavy-heating days, sun follows the date.
Eco-score & badges
A 0–100 score from real data (self-sufficiency 45%, net-seller days 35%, gas-free days 20%) with levels and achievements like Solar Baron and Flame Tamer.
What-if simulator
Sliders for extra panels, battery size and a heat pump replay the real 366 days under a new configuration — new bill, savings, payback years and CO₂ avoided.
Living house
Evening window lights follow a household routine — kitchen first, bedrooms last, lights out near midnight.

## Slide 12
STANDARDS 12
Bram House · Building-Level Digital Twin
Standing on open standards
Interoperability is the point of the 3DxVERSE testbed
IFC (ISO 16739)
single source of truth for geometry & room identity (GUIDs preserved end-to-end)
OGC 3D Tiles
streaming format for the building shell and 3D BAG context
GeoJSON + WGS84
room footprints and every coordinate in the app (EPSG:4326)
PDOK / 3D BAG
Dutch national open data (CC-BY) for imagery and neighbours
OGC SensorThings
planned standard for the live indoor-sensor feed
Replicable by design: any EU community with a BIM model and meter exports can rebuild this pipeline.

## Slide 13
LESSONS 13
Bram House · Building-Level Digital Twin
What the build actually taught us
The honest engineering notebook
1.
Georeferencing is never free
The ion tiler ignored IfcSite in IFC2x3 — the model landed at (0,0). Manual east-north-up anchoring with configurable heading/height solved it.
2.
Big files hide small data
All 21 rooms lived in the first 53 KB of the 474 MB IFC. Slicing before parsing turned minutes into seconds.
3.
Clipping planes have their own world
Cesium anchors clip planes in the tileset's frame, not the world — one bad matrix made the whole model vanish. Distance calibration beats matrix surgery.
4.
Meters are cumulative
Summing readings double-counts massively; totals must be last-minus-first with reset guards.
5.
Cloud sync fights developers
OneDrive appended NUL bytes to five source files mid-edit, silently breaking room navigation. Version control and non-synced dev folders are not optional.

## Slide 14
Where it goes next
Live sensors
indoor CO₂ / temperature / humidity via OGC SensorThings, joined on room_id
Room-level energy
sub-metering mapped through the prepared room_energy_mapping.json
Hardening
TypeScript, tests for the meter math, CI, scoped ion tokens, git
Deployment
hosted at twinlink.eu as the Aadorp node of the Local Digital Twin
Bram House · Twinlink.eu · 3DxVERSE D7.2 · University of Twente / ITC
Thank you